## Slide 1: SITE PLANNING 101
EVERY PROJECT STARTS AS A SITE
ORB University
ORB UNIVERSITY – MARCH 29, 2023
PRESENTED BY Tim Rice and Peter Gormley

## Slide 2: INITIAL SITE DATA
American Land Title Association (ALTA) Survey
  Owner Provided
  Attached to the Property Sale/ Title Documents
  Meets & Bounds/ Property Line (Net)
    Coordinates and Segment Lengths
  Established Easements
    Right-of-Way
    Utility

## Slide 3: INITIAL SITE DATA
INITIAL SITE DATA
Legal Description
  Owner Provided
  Exhibit to Property Sale/ Title Documents
  Describes Meets & Bounds/ Property Line (Net)
    Coordinates and Segment Lengths
    Should Match those on ALTA Survey
  Updated to conditions present at the time of sale
  Required to be included, verbatim, on Site Plan submittals

## Slide 4: INITIAL SITE DATA
COUNTY ASSESSOR PARCEL MAP
  Provides Assessor Parcel Number (APN)
    Standard Nationwide
  Lists recorded parcel area (NET)
    Measured to buried markers
    Sometimes use permanent site features
      Fire Hydrants
      Shared Utility Equipment
    Different documents may state area differently
    City will follow area STATED on the Site Plans
  Property Owner’s Name & Address
    Can lag following sale
    Name, Address & Contact must be provided on applications
      Owner Authorization Form
  Used to generate Buffer Maps/ Mailing Lists
  Current Property Zone

## Slide 5: INITIAL SITE DATA
DIGITAL MAPPING
  Most current as-built conditions in most cases
    Existing Structures
    Site Features
    Utility Equipment
    Surrounding Context
  City of Phoenix allows marked up view as Preliminary Application Site Plan

## Slide 6: ZONING
Zoning Code
  Defines all Zone Classifications and uses permitted and conditions site must confirm to within a particular area
    Can be Municipality or County
    Sections are cross referenced to each other
Zoning Class Definitions
  Includes (but not limited to)
    Uses Allowed
    Building Height
    Lot Coverage
    Building Setbacks
    Multi-family unit density
    Parking density required
Zone must include all planned uses
  In current development
  Future expansion
  Re-zoning processes vary
    Hearings at various levels
    Public notifications/ meetings
    Need to be considered in project schedule
  Re-zoning efforts are NEVER guaranteed

## Slide 7: Building Type Considerations
Mixed Use Sites
  What are the building types and uses being included on the parcel?
    This is dictated by the owner/developer’s proforma
    Mixed-Use Sites
      More than one use needs to be considered by separate Building
    Mixed-Use Buildings
      All uses within one building need to be considered overall
Building Types
  Garden
  Wrap
  Townhome
  Podium
  Amenity Building – Clubhouse/Leasing
    Mixed-use within one building

## Slide 8: Parking Considerations
Surface Parking vs. Parking Garages
  Commonalities (defined by county or municipal codes)
    Standard stall dimensions
      90 degrees
      Angled
      Parallel
      Single/Tandem
    Aisle Widths
      Mono or Bi-Directional
      Vary based on stall direction
      If part of Fire Access Route – City will typically determine required width
    Overall Stall Counts
    By Unit Type (number of bedrooms) and Count for Multi-Family
    By Usage and Square Feet for other Uses

## Slide 9
ADA Parking Stalls
Should always be located in the most convenient location for the user traveling to their final destination point.
When possible, accessible spaces should always be located in covered areas.
Stall Size
Loading Aisles – size determined by municipality
Signage
Surface Markings
Counts
2% of each type provided
Mandated by ANSI 117A
Access via Accessible Path of Travel

## Slide 10
Surface Lot Considerations
  Landscaping Islands
    Width
    Planting Materials
    Planting Coverage
    Frequency
      Number of spaces between islands
  Parking Shade Covers
    Ratio of Covered vs. Open
    ADA requires 2% or equal to overall ratio of covered to open
Parking Garage Considerations https://www.pci.org/PCI_Docs/Project_Resources/Parking_Structures/Parking%20Structures%20Recommended%20Practice%20in%20Design%20and%20Construction.pdf

## Slide 11
Parking Garage Considerations https://www.pci.org/PCI_Docs/Project_Resources/Parking_Structures/Parking%20Structures%20Recommended%20Practice%20in%20Design%20and%20Construction.pdf
Ground Level Location
  Surface
  Underground
Ventilation
  Open
  Mechanically Ventilated
  IBC 406.5

## Slide 12
Minimum Overhead Height Clearance
  Construction Method
    PreCast Double Tees
    T-Pac
    Coreslab
  Floor-to-Floor Height
    Van Accessible requires 8’-2” Min.
Maximum Efficiency
  +/-308 sf/car
Mechanical & Plumbing
  Sprinklers
  Lighting
  Piping for units built overhead
Ramps
  Width
  Length
    Ramp length of 160’-180’ most efficient
  Slope
    Speed Ramps typically <14%
    May require transition slope at top and bottom.
    Maximum slope of a ramp that incorporates parking 6.67%

## Slide 13
Ventilation
  Open
    Area open to the Outside
    Minimum SF defined by IBC Section 406.5
  Closed
    Needs Mechanical Ventilation
      More costly than Open structure
Floor-to-Floor Alignment
  Considered in a wrap building
  Occupancy Separations
Pedestrian Access
  Stairs
  Elevators
  Ramps

## Slide 14: Loading Zones
10’x30’ Dedicated for Loading Only
  Verify with municipality
    Part of Phoenix Zoning Code Section 702 Off-Street Parking and Loading
  Striped Area
  Posted for Loading Use and No Parking Allowed
  Do not require deceleration or pull-in/out lanes
  Number of zones required determined by overall unit count

## Slide 15: Solid Waste Disposal
Can be a department separate from Planning and Zoning Departments or private collector
  Can require separate submittal, review, and approval
Surface / Garden Sites
  Municipality may have developed set of guidelines
  Bin size and number required can be a calculated volume
    By unit count / size
    By square footage
  Bin enclosure design can be mandated by code
    Most are similar, but can be unique & varied
    Must be determined by municipality

## Slide 16
Collection Vehicle Access Requirements
  Security Gate Access
  Turning Radii
  Drive Aisle Width
  Defined Access Route
  Enclosure Approach Angle
Parking Garages / High Rises
  Trash Chutes
  Termination Bins / Compactors
    Collection Vehicle Access

## Slide 17: Site Accessibility
Accessible Path of Travel
  Provided from Building Egresses
  To Accessible Parking
Accessible Pedestrian Route
  Through Entire Site
  Must Connect to Public Way
  To Provided Site Amenities
    Amenities Building (Clubhouse)
    Playgrounds
    Pool / Spa
    Central Mailboxes
    Parcel / Package pick-up rooms
    Trash Enclosures
    Central Laundries

## Slide 18
Walkways
  Defined system to interconnect all parts of the development
  May be required to connect to larger system
    City Walkways
    Trail and Path System
  Have defined methods of Construction Allowed
  Width
    Minimum is 3’-0” for ADA access
    5’-0” is most common, unless unable
  Allowed to slope for drainage
  Ramps
    Max. slope of 1:12
    Max. rise for any run 30”
      5’ Landings used to break up runs
    Handrails are required
  Stairs
    Handrail required for more than (2) steps
    (2) risers with (1) tread are allowed within path of travel
      Can be safety rolled over
  Curb Step Offs
    Accessible ramp must be provided at curb step-off along Path of Travel
    Designs are mandated by municipality codes
      Depth/ slope and surface treatment can vary

## Slide 19: Vehicle Access/ Parking Screening/ Landscape/ Utilities
Utilities
  Typically located within existing underground easements
  New services are not allowed to cross property lines
    Can be allowed as part of a signed and recorded Access Agreement
  Electrical Transformers
    Require access from Utility Department
    Coordinated directly with utility provider
      Separate submittal and approval process
    Proximity to buildings a consideration
      Considered hazardous
      Mandated by utility
        Based on capacity of transformer
      Require rated protection if placed too close
    Often required to be screened
      Physical barrier
      Landscaping

## Slide 20
Parking Lot Screening
  Most parking is required to have screening of stalls
    Wall and/or fence designs may have design standards imposed by municipality
    Heights are mandated to prevent view obstruction
      Low walls used to prevent headlight glare
      Visibility Triangles
    Fences/ Walls with Security Gates
      Gates may have design standards imposed
      Must provide Queuing Distance
        Space for gates to open
        Does not allow traffic to obstruct public ways
      Operable for emergency, solid waste, utility and mail services
        Also for delivery and ride sharing services
Landscaping
  Minimum Coverages
    Shade can be mandated
  Species Allowed
    Determined in conjunction with inventory/ Salvage submittal process
  Landscape Buffers
    Can be mandated as Setback requirements
  Parking Islands
    Size of island
    Planting volume required
    Frequency between stalls

## Slide 21: FIRE DEPARTMENT ACCESS
Access Loop
  Circular route through entire site
  Access to all buildings
  Min. aisle widths must be maintained
    Kept clear via signage and curb painting
    20’ typically
      18’ min. in some jurisdictions
      Mono direction
      Fire Only Lanes
  Turning Radius
    Minimum inside, center and outside dimensions
    Dimensioned on Site Plan/ Fire Access Plan

## Slide 22
Dedicated Fire Lanes
  Minimum Widths
  Maximum lengths to dead ends
    Under 150’ to back out
    Turn-around or cul-de-sac required for longer lanes
  Required when buildings are more than 250’ from Fire Access Route
  Can be of alternative materials
    Decomposed granite
    Grass Paving systems
Building Addressing
  Approved Addressing Exhibit required with Site Plan
    Must be approved as will be used in Fire Alarm Panel and 911 notifications
  Building Address Signage
    Location must follow the standards of the Fire Department/ Jurisdiction
    Locations shown on Exterior Elevations
    Minimum standards for letter/ character heights
      High contrast
      Font
    Must match approved Addressing Exhibit

## Slide 23
Hydrants
  Existing Public hydrants located on Site Plan
    Also on Civil Utility and ALTA Surveys
    Flow Test required to confirm pressure at existing hydrants
  Private hydrants are required on site
    Spacing mandated by City codes
      From nearest public hydrant
      Between locations on site
Fire Riser Rooms
  Identified on building exterior by signage
  Accessible from building’s exterior
  Remote Fire Department Connections (FDC) may be required
    If room is located too far from hydrant