## Slide 1: COMMON ACCESSIBILITY CHECKLIST
ORB University
ORB UNIVERSITY – JUNE 05, 2024
PRESENTED BY Theodore Cannon
ANSI VS. ADA
&
Notes: ASD ASD FASDF ASD FASFD

## Slide 2: THE PURPOSE OF THIS PRESENTATION
To better understand ANSI and ADA as they relate to common area spaces.
To view common area accessibility in current ORB projects.
To give a generalized overview of the importance of the ORB accessibility checklist.

## Slide 3: BACKGROUND: ACCESSIBILITY STANDARDS FOR COMMON AREAS
Building code (IBC, referencing ANSI A117.1)
Americans with Disabilities Act Standards for Accessible Design (ADA)
Notes: TWO main sources for accessibility standards that influence how we design and inspect the common areas in our projects.

## Slide 4: *FOR MORE ACCESSIBILITY INFORMATION
Terry Kitay “Housing Accessibility” presentation is located on the server in the ORB Resource Library > Accessibility Items
“ Theresa L. "Terry" Kitay focuses her practice on defense and preventive representation of clients in the housing industry in all civil rights matters.”
- Baker Donelson Website.

## Slide 5: WHEN TO USE ANSI
Common area spaces outside of the leasing area
Accessible Type A and Type B units.
The surrounding site. IE: Crosswalks, accessible paths, gates, etc.

## Slide 6
ACCESSIBILE SITE INSPECTIONS

## Slide 7: WHEN TO USE ADA
Applies to commercial facilities and "places of public accommodation" (Title III)
Applies to "programs" of state and local governments (Title II)
Limited application to housing (except publicly funded housing)
Limited application to multifamily: just “places of public accommodation” (Title III)
Excerpt from Terry Kitay’s Accessibility Presentation

## Slide 8: WHATS THE DIFFERENCE?
Both ANSI and ADA have similar applications, so how do I know when to use one or the other?
ADA: Limited application to multifamily: just “places of public accommodation” (Title III)
  Leasing office(s)
  Restroom(s) serving Leasing
  Parking serving Leasing
Notes: The only major difference is in the restroom(s) serving leasing. They have slight variations in toilet paper holder placement, AND grab bar installation is required.

## Slide 9: SLIGHT DIFFERENCES
ADA Figures 604.5.2
ANSI Figures 604.5
ANSI requires the installation of a vertical grab bar at common access restrooms, ADA does not. ORB often opts for the most restrictive version.
SIDE
FRONT

## Slide 10: SLIGHT DIFFERENCES
ADA Figure 604.7
ANSI Figure 604.7.1(A)
Toilet paper dispensers have slight differences in their placement requirements. ORB often opts for the most restrictive version.

## Slide 11: BROADSTONE UPTOWN

## Slide 13
GRAB BAR TO BE PLACED
OPEN KNEE SPACE
COUNTER HEIGHT – 34”
TP DISPENSER TO BE PLACED

## Slide 15
KNEE SPACE
COUNTER HEIGHT
WORK ROOM (GRAY AREA)
ANSI or ADA?

## Slide 19: BROADSTONE on 7th

## Slide 21
WORK ROOM (GRAY AREA)
COUNTER HEIGHT
OUTLET HEIGHT
ANSI /ADA 44”
Notes: Why is the work room a gray area?

## Slide 22: THE ANSI/ADA DETAIL
FIGURE 308.2.2
Most relevant code elements applicable to our projects are the same across both ANSI and ADA.

## Slide 23: THE COMMON AREA FINISH CHECKLISTS

## Slide 24: CHECKLIST LOCATION (IF APPLICABLE TO PROJECT)
When required, the checklists are/will be located in the following location.
T: Drive > ORB > ORB Resource Library > Accessibility items > Current Checklist > Common Area Checklist > Finish Checklists
Notes: ORB will not be contracted to complete Accessibility Services for every project. …
*SEE ORB CHECKLIST IN ORB UNIVERSITY FOLDER

## Slide 25: THE POOL AREA – CHECKLIST REVISION
Upon walking and inspecting Karen and I were made aware of an important inspection item required by our life safety…
EXCERPT FROM COMMON AREA EXTERIOR CHECKLIST
VS

## Slide 26: BROADSTONE UPTOWN

## Slide 27: BROADSTONE UPTOWN

## Slide 28: BROADSTONE UPTOWN

## Slide 34: A COUPLE OF AREAS OF NON-COMPLIANCE

## Slide 35
BROADSTONE UPTOWN
Notes: Originally the “pull clearance” requirement was not satisfied for this condition. The gate was about 1 – 2 feet farther back originally. 18” on the latch side is necessary, so this gate had to be moved.

## Slide 36
BROADSTONE UPTOWN
BROADSTONE DOBSON RANCH
Notes: Originally the “pull clearance” requirement was not satisfied for this condition. The gate was about 1 – 2 feet farther back originally. 18” on the latch side is necessary, so this gate had to be moved.